## Slide 1: EN 261: Part Two
Welcome back from spring break!
xkcd.com/1007/

## Slide 2: Recap
Cost/Benefit Analysis
Decision Trees
Discounting
SMART
Sensitivity / Uncertainty Analysis

## Slide 3: What’s Next? (7 more weeks!)
Spatial Interpolation of Environmental Variables (Today)
Aggregation Techniques for Risk Assessment
GIS & Decision Making
AHP
LISA Analysis
Optimization Modeling
Two guest speakers:
  Chi Ho Sham, Vice President, The Cadmus Group
  Sam Ratick, Professor, Clark University (Formerly Operations Research Analyst, EPA)

## Slide 4: Common Feedback from Jan/Feb
Want to see more of the “under the hood” stuff – how would you arrive at the values /data that are given in the assignments?
Assignments can sometimes be very hard to do in groups, logistically and otherwise.

## Slide 5: Logistics
Reading Assignment 4 is due Mon Mar 19th.
Problem Set 2 will be given out this Wednesday, due Wednesday, Mar 28.
Both assignments are individual: everyone must turn their own assignment in.

## Slide 6: Spatial Interpolation

## Slide 7: Today’s Goals
What is spatial interpolation?
What are some examples of spatial interpolation?
What are a few different types of interpolation?
What else do I need to know?

## Slide 8: Spatial Interpolation
 | 8 |  | 8 | 
 |  |  |  | 12
 |  | 12 |  | 
# | Sample
# | Estimation

## Slide 9: Spatial Autocorrelation
Things closer together are more similar than those farther apart.
1 | 0 | 1 |  | 3
1 | 1 | 1 | 3 | 4
3 | 2 | 2 | 4 | 
4 | 3 |  | 5 | 6
5 | 4 | 5 | 6 | 7
The red and purple cells are more likely to be similar than the red and blue cells.

## Slide 10: Today’s Goals
What is spatial interpolation?
What are some examples of spatial interpolation?
What are a few different types of interpolation?
What else do I need to know?

## Slide 11: Day-to-day examples

## Slide 13: Environmental Examples
Estimates of Potential Nitrogen Runoff using Polygonal Interpolation
Sample Cell

## Slide 14: Environmental Examples
Sample Cell
Sample Cell
Estimates of Potential Nitrogen Runoff using IDW

## Slide 15: Environmental Examples
Sample Cell
Estimates of Potential Nitrogen Runoff using Ordinary Kriging

## Slide 16: Today’s Goals
What is spatial interpolation?
What are some examples of spatial interpolation?
What are a few different types of interpolation?
What else do I need to know?

## Slide 17: Types of Spatial Interpolation
Polygonal
Inverse Distance Weighting
Kriging
Splining
Regression Kriging
Co-Kriging
Natural Neighbor
….. and more!

## Slide 18: Types of Spatial Interpolation
Polygonal
Inverse Distance Weighting
Kriging
TIN
Splining
Regression Kriging
Co-Kriging
Natural Neighbor
….. and more!

## Slide 19: Polygonal Interpolation
Simple. Ideal when you suspect neighbors are extremely similar.
Each un-sampled cells is given the value of the closest sample.
 | 8 |  | 8 | 
 |  |  |  | 12
 |  | 12 |  | 
# | Sample
# | Estimation

## Slide 20
 | 8 |  | 8 | 
 | 12 |  |  | 12
 |  | 12 |  | 
Process:
Identify the closest cell to the unknown point you are interested in estimating.
Assign that value to the unknown point.

## Slide 21: Inverse Distance Weighting
More complex than Polygonal. A good choice if you know, theoretically, how quickly things become less similar (e.g., elevation tends to drop off at predictable rates in many places).
Each unknown point is given a value according to a WLC of other known points.
8 | 8 | 8 | 8 | 8
8 | 9 | 9 | 10 | 11
10 | 10 | 11 | 11 | 12
11 | 12 | 12 | 12 | 12
12 | 12 | 12 | 12 | 12

## Slide 22: Inverse Distance Weighting
You don’t need to memorize these equations! But it will be helpful to know how it works for interpretation of your results.
Essentially, each unknown point has a value assigned to it based on the value of each known point, and the distance between the unknown point you want to estimate and all known points. The weight assigned to each known point is calculated in equation 2.

## Slide 23
 | 8 |  | 8 | 
 | ? |  |  | 12
 |  | 12 |  | 
Process:
Calculate the distance between the point you want to estimate and all known points.
Determine the weight for each point by applying the equation: “1/d^p”
Multiply the weights by each value.
Divide this sum by the sum of weights.

## Slide 24
 | 2 |  | 2.8 | 
 | ? |  |  | 3
 |  | 1.4 |  | 
Process:
Calculate the distance between the point you want to estimate and all known points.
Distances from unknown cell

## Slide 25
 | .25 |  | .13 | 
 | ? |  |  | .11
 |  | .51 |  | 
Process:
Calculate the distance between the point you want to estimate and all known points.
Determine the weight for each point by applying the equation: “1/d^2”
The yellow cell is 2 units away from the unknown red cell. Thus, its weight is (1/[2^2]), or 0.25.
Distances from unknown cell

## Slide 26
 | 2 |  | 1.0 | 
 | ? |  |  | 1.3
 |  | 6.1 |  | 
Process:
Calculate the distance between the point you want to estimate and all known points.
Determine the weight for each point by applying the equation: “1/d^2”
Multiply the weights by each value.
The original value in the yellow cell was 8. We multiply that by the distance weight, .25. 8*0.25 = 2.
Distances from unknown cell

## Slide 27
 | 2 |  | 1.0 | 
 | ? |  |  | 1.3
 |  | 6.1 |  | 
Calculate the distance between the point you want to estimate and all known points.
Determine the weight for each point by applying the equation: “1/d^p”
Multiply the weights by each value.
Divide this sum by the sum of weights.
Distances from unknown cell
Numerator: 2 + 1.0 + 6.1 + 1.3 = 10.4
Denominator: .25 + .51 + .13 + .11 = 1.0
Final Estimate: 10.4 / 1.0 = 10.4!

## Slide 28: Ordinary Kriging
Very complex. Useful when you have no theoretical knowledge of spatial autocorrelation, as this method uses your sample to estimate autocorrelation.
Also creates a WLC
8 | 8 | 8 | 8 | 8
8 | 9 | 8 | 9 | 9
9 | 9 | 9 | 12 | 12
11 | 12 | 12 | 12 | 12
12 | 12 | 12 | 12 | 12
# | Sample
# | Estimation

## Slide 29: Kriging
A two step process. First, spatial autocorrelation is estimated from known points following the first equation.
Second, the weights from each known point to each unknown point are solved for on the basis of the autocorrelation you measure in the first step.

## Slide 30: Triangulated Irregular Networks (TIN) AKA Delaunay Triangles
A refined version of the Polygonal technique. Useful when you know neighbors tend to be more similar.
Creates values based on the three closest known point to any unknown point.

## Slide 31: Today’s Goals
What is spatial interpolation?
What are some examples of spatial interpolation?
What are a few different types of interpolation?
What else do I need to know?

## Slide 32: Limitations
Spatial Interpolation only makes sense when there are spatial patterns in the data.
They are only valid within a single study domain (e.g., if you had weather stations in Alabama, you could not use them to interpolate weather data in Georgia).
Estimates are stronger when spatial autocorrelation is more prevalent.

## Slide 33: Validation
Two types of validation are common:
  Cross-validation: re-estimate the results over and over again by dropping one point out of the analysis and predicting what its value is. Error is estimated on the basis of all of these validations.
  Calibration/Validation: Intentionally use a portion of your data for calibrating only, and a portion of your data for validation only.

## Slide 34: Reading Assignment 4
You will be using multiple interpolative methods to predict precipitation in the Plum Island Ecosystems, an area just north of Boston, MA.
You will compare the results of each method, and write why you think those differences occur.
This is NOT a group assignment: everyone must turn in their own!